CCIE Routing and Switching Practice Labs

ISBN: 1-58705-147-8

Cisco Press

# Errata

Page 34 – “will cause R3 to now unicast its routing updates directly to R2”

Page 35 – “The lab rules are also no static routes”

Page 43 – Top of page “visibility if” should be visibility of.

Page 45 – First note on the page: “There is no ebgp-multihop”

Page 50 – In example 1-40 the second route-map should read “route-map 20.20.20.0 permit 20”

Page 59 – The final access-list in Example 1-60 should read “access-list 100 permit ip 10.50.50.0  0.0.0.7 any”

Page 62 – Second paragraph – “The stub router does not fully participate”

Page 100 – Near bottom of page – Bullet statement “inject at” should be “inject a”

Page 111 – top of page – “ISDN as itis” should reach ISDN as it is.

Page 114 – Large paragraph – 5th line down – “that isa private” should be – that is a private

Page 114 – 8th line in the same paragraph as above reads “system to another about when the keyword remove-private-AS.” The word “about” is not required and should be removed.

Page 148 – The last bulleted paragraph under the heading ‘Section 6: DLSw+ (6 Points)’ should read, “R4

and R5 should show reachability of NetBIOS name ccie???? Advertised from R6.  This is the

only NetBIOS name of which R6 should have visibility.”

Page 186 – The last bulleted paragraph on the page should read, “R4 and R5 should show reachability of

NetBIOS name ccie???? Advertised from R6.  This is the only NetBIOS name of which R6

should have visibility.”

Page 197 – Regarding Example 3-93, the access-list should read:

!

access-list 115 deny tcp any any eq 135 log-input

access-list 115 deny udp any any eq 135 log-input

access-list 115 deny tcp any any eq 139 log-input

access-list 115 deny udp any any eq 139 log-input

access-list 115 deny tcp any any eq 445 log-input

access-list 115 deny udp any any eq 445 log-input

access-list 115 permit ip any any

Page 283 – Replace figure 5-10 with the following illustration: