CCNP and CCIE Enterprise Core & CCNP Advanced Routing Portable Command Guide: All ENCOR (350-401) and ENARSI (300-410) Commands in One Compact, Portable Resource

First Edition

Copyright© 2020 Cisco Systems, Inc.

ISBN-10: 0-13-576816-0
ISBN-13: 978-0-13-576816-7

Warning and Disclaimer

Every effort has been made to make this book as complete and as accurate as possible, but no warranty or fitness is implied. The information provided is on an "as is" basis. The author and the publisher shall have neither liability nor responsibility to any person or entity with respect to any loss or damages arising from the information contained in this book or from the use of the CD or programs accompanying it.

When reviewing corrections, always check the print number of your book. Corrections are made to printed books with each subsequent printing.

First Printing: April 2020

Corrections for Feb 19, 2024

| Pg | Error – First Printing | Correction |
| --- | --- | --- |
| 331 | Last two lines of the table should read: CE2(config-if)# ospfv3 1 ipv4 area 2 Assigns the Loopback 0 interface to area 2 for the OSPFv3 IPv4 address family CE2(config-if)# ospfv3 1 ipv6 area 2 Assigns the Loopback 0 interface to area 2 for the OSPFv3 IPv6 address family |
| 208 | Correct IP address in table should read as: DLS1(config-ip-sla)# icmp-echo 209.165.201.1 Configures the SLA as an ICMP echo operation to destination 209.165.201.1 |
| 215 | The correct value is gigabitethernet 0/0/1 R1(config-if)# interface gigabitethernet 0/0/1 Enters interface configuration mode |
| 80 | The correct router prompt: Router(config-rtr)# metric weights tos k1 k2 k3 k4 k5 Changes the default K-values used in metric calculation. These are the default values: tos=0, k1=1, k2=0, k3=1, k4=0, k5=0 |
| 84 & 85 | Currently reads: Correction: Configuration Example: EIGRP for IPv4 and IPv6 Using Named Mode Figure 4-1 shows the network topology for the configuration that follows, which shows how to configure EIGRP using commands covered in this chapter. The example assumes the IPv6 unicast routing is already enabled on R1, R2 and R3. |

This errata sheet is intended to provide updated technical information. Spelling and grammar misprints are updated during the reprint process but are not listed on this errata sheet.