Cisco Voice over IP (CVoice) (Authorized Self-Study Guide)

ISBN: 1-58705-262-8

Cisco Press

# Errata

(**Note** Corrections noted to pages 31, 157, 181, 365, 382 and 417 were contributed by Aaron Gould, Communications Systems Engineer of Northrop Grumman.)

Page 31, Figure 1-21:

Should read as follows:

“CAS” should be “CSS”

Page 56, Figures 2-12

Reads:

“E&M Type I”

Should read:

“E&M Type V”

Page 56, Figure 2-13

Reads:

“E&M Type V”

Should read:

“E&M Type I”

Page 157, Example 4-3:

Dial peer 2 should be a voip dial peer, as opposed to a pots dial peer.

There should not be a space between ‘ipv4:’ and ’10.18.0.1’ at the bottom of the example.

Page 181, Example 4-21:

Dial peer 44 should be a pots dial peer, as opposed to a voip dial peer.

Page 181, Example 4-22:

Dial peer 55 should be a pots dial-peer, as opposed to a voip dial peer.

Page 365, Last sentence:

Should read – “Therefore, configure the gatekeeper to recognize 1# as a default technology prefix with the gw-type-prefix 1#* default-technology command.”

Page 382, Bullet:

Reads as: “The WAN or WAN protocol can use the following QoS mechanisms:”

Should read: ‘The WAN interface can use the following QoS mechanisms.”

Page 417, Chapter 1, Question 7:

Answer to Question 7:

Should be ‘d’ instead of ‘c’

Page 417, Chapter 1, Question 8”

Answer to Question 8:

Should be ‘c’ instead of ‘b’